## Slide 1: PlaqueQuant – Blood Vessel stenosis quantification software
7 Jun 2016

## Slide 2: Project Scope
PlaqueQuant is a software with various algorithms, which facilitates user to perform accurate segmentation of blood vessels. Quantitative analysis are performed to help user to quantify blood vessel stenosis
The following steps are used to demonstrate the robustness of the software
Step 1: Loading anatomical images
Step 2: Introduction of the main user interface
Step 3: Segmentation
Step 4: Analysis - 2D and 3D View
Step 5: Report

## Slide 3: Loading Anatomical Images
User can add anatomical images such as
  CUBE T1 image
  CUBE T2 image
  CUBE T1 + Contrast
  2D Double Inversion Recovery (DIR)/Quadruple inversion recovery (QIR)
  MPRAGE
Rigid Alignment for the image will be performed in the background

## Slide 4: Introduction of the main UI
Basic Navigation
Cursor Tools
Contrast Tools
Ruler Tools
Sagittal
Coronal
Axial
3D
Tool bar
Segmentation Window
Slice
3D View Option
Menu bar

## Slide 5: Introduction of the main UI
User can anytime switch from traditional multiple angle view to all axial view, which can display maximum three image data at the same time
User will find it easier to perform segmentation in all axial view
Axial
Axial
Axial
Select the display image
Switch the View

## Slide 6: Segmentation
Region of Interest selection tool:
  User can define the blood vessel which is of your interest. Subsequent operations are applied to this ROI

## Slide 7: Segmentation
In the segmentation stage, we use different tools to segment different parts of the blood vessel
  Contour Widget (for Vessel Wall and Lumen)
  Brush Widget(for Plaque)

## Slide 8: Segmentation
Contour Widget
  We use contour widget to select the vessel wall and lumen, layer by layer, highlight the corresponding region
  We can also calculated the wall thickness
Maximum wall thickness

## Slide 9: Segmentation
Brush Tool
We can use the brush tool to highlight plaque, such as calcification, hemorrhage, lipid-rich necrotic core, and loose matrix

## Slide 10: Analysis - 2D results
Measurement and Analysis
Lumen, Vessel Wall, Plaque Area
Maximum Wall Thickness
Normalized Wall Index

## Slide 11: 3D measurement of vessel stenosis
  After manual segmentation in 2D viewer, 3D model is automatically generated.
  Use can use 3D ruler tool to interactively measure stenosis length (A) and reference length (B)
  % stenosis

## Slide 12
A pdf report is generated on request. 2D, 3D segmentation measurement, images, different statistics such as the maximum wall thickness and % stenosis are included in this report